## Slide 1: Computer Architecture and Operating Systems Lecture 8: Memory and Caches
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Processor-Memory Performance Gap
Computer performance depends on:
  Processor performance
  Memory performance

## Slide 3: Memory Challenge
Make memory appear as fast as processor
Ideal memory:
  Fast
  Cheap (inexpensive)
  Large (capacity)
But can only choose two!

## Slide 4: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $2000 – $5000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $20 – $75 per GB
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk

## Slide 5: Locality
No need for large memory to access it fast
Just exploit locality
Temporal Locality:
  Locality in time
  If data used recently, likely to use it again soon
  How to exploit: keep recently accessed data in higher levels of memory hierarchy
Spatial Locality:
  Locality in space
  If data used recently, likely to use nearby data soon
  How to exploit: when access data, bring nearby data into higher levels of memory hierarchy too

## Slide 6: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU

## Slide 7: Memory Hierarchy
Personal mobile device
Laptop or desktop
Server

## Slide 8: How It Works?
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level
Processor
L1
L2
Memory

## Slide 9: Hits and Misses
On cache hit, CPU proceeds normally
On cache miss
  Stall the CPU pipeline
  Fetch block from next level of hierarchy
  Instruction cache miss
    Restart instruction fetch
  Data cache miss
    Complete data access

## Slide 10: Miss Types
Compulsory: first time data accessed
Capacity: cache too small to hold all data of interest
Conflict: data of interest maps to a location in cache mapped to different data

## Slide 11: Memory Performance
Hit: data found in that level of memory hierarchy
Miss: data not found (must go to next level)
  Hit Rate = # hits / # memory accesses = 1 – Miss Rate
  Miss Rate = # misses / # memory accesses = 1 – Hit Rate
Average memory access time (AMAT): average time for processor to access data
  AMAT = tcache + MRcache[tMM + MRMM(tVM)]

## Slide 12: Cache Memory
Cache memory
  The level of the memory hierarchy closest to the CPU
Given accesses X1, …, Xn–1, Xn
How do we know if the data is present?
Where do we look?

## Slide 13: Direct Mapped Cache
Location determined by address
Direct mapped: only one choice
  (Block address) modulo (#Blocks in cache)
#Blocks is a power of 2
Use low-order address bits
Cache
Memory

## Slide 14: Tags and Valid Bits
How do we know which particular block is stored in a cache location?
  Store block address as well as the data
  Actually, only need the high-order bits
  Called the tag
What if there is no data in a location?
  Valid bit: 1 = present, 0 = not present
  Initially 0

## Slide 15: Direct Mapped Cache Example
8-blocks, 1 word/block, direct mapped
Initial state
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | N |  | 
111 | N |  | 

## Slide 16: Direct Mapped Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | N |  | 
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Miss | 110

## Slide 17: Direct Mapped Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
26 | 11 010 | Miss | 010

## Slide 18: Direct Mapped Cache Example
Index | V | Tag | Data
000 | N |  | 
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | N |  | 
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
22 | 10 110 | Hit | 110
26 | 11 010 | Hit | 010

## Slide 19: Direct Mapped Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 11 | Mem[11010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
16 | 10 000 | Miss | 000
3 | 00 011 | Miss | 011
16 | 10 000 | Hit | 000

## Slide 20: Direct Mapped Cache Example
Index | V | Tag | Data
000 | Y | 10 | Mem[10000]
001 | N |  | 
010 | Y | 10 | Mem[10010]
011 | Y | 00 | Mem[00011]
100 | N |  | 
101 | N |  | 
110 | Y | 10 | Mem[10110]
111 | N |  | 
Word addr | Binary addr | Hit/miss | Cache block
18 | 10 010 | Miss | 010

## Slide 21: Associative Caches
Fully associative
  Allow a given block to go in any cache entry
  Requires all entries to be searched at once
  Comparator per entry (expensive)
n-way set associative
  Each set contains n entries
  Block number determines which set
    (Block number) modulo (#Sets in cache)
  Search all entries in a given set at once
  n comparators (less expensive)

## Slide 22: Associative Cache Examples

## Slide 23: Spectrum of Associativity
For a cache with 8 entries

## Slide 24: Associativity Example
Compare 4-block caches
  Direct mapped, 2-way set associative, fully associative
  Block access sequence: 0, 8, 0, 6, 8
Direct mapped
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | 0 | 1 | 2 | 3
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[8] |  |  | 
0 | 0 | miss | Mem[0] |  |  | 
6 | 2 | miss | Mem[0] |  | Mem[6] | 
8 | 0 | miss | Mem[8] |  | Mem[6] | 

## Slide 25: Associativity Example
2-way set associative
Block address | Cache index | Hit/miss | Cache content after access |  |  | 
 |  |  | Set 0 |  | Set 1 | 
0 | 0 | miss | Mem[0] |  |  | 
8 | 0 | miss | Mem[0] | Mem[8] |  | 
0 | 0 | hit | Mem[0] | Mem[8] |  | 
6 | 0 | miss | Mem[0] | Mem[6] |  | 
8 | 0 | miss | Mem[8] | Mem[6] |  | 
Fully associative
Block address |  | Hit/miss | Cache content after access |  |  | 
0 |  | miss | Mem[0] |  |  | 
8 |  | miss | Mem[0] | Mem[8] |  | 
0 |  | hit | Mem[0] | Mem[8] |  | 
6 |  | miss | Mem[0] | Mem[8] | Mem[6] | 
8 |  | hit | Mem[0] | Mem[8] | Mem[6] | 

## Slide 26: How Much Associativity
Increased associativity decreases miss rate
  But with diminishing returns
Simulation of a system with 64KB D-cache, 16-word blocks, SPEC2000
  1-way: 10.3%
  2-way: 8.6%
  4-way: 8.3%
  8-way: 8.1%

## Slide 27: Replacement Policy
Direct mapped
  No choice
Set associative
  Prefer non-valid entry, if there is one
  Otherwise, choose among entries in the set
Least-recently used (LRU)
  Choose the one unused for the longest time
    Simple for 2-way, manageable for 4-way, too hard beyond that
Random
  Gives approximately the same performance as LRU for high associativity

## Slide 28: Write-Through
On data-write hit, could just update the block in cache
  But then cache and memory would be inconsistent
Write through: also update memory
But makes writes take longer
  e.g., if base CPI = 1, 10% of instructions are stores, write to memory takes 100 cycles
    Effective CPI = 1 + 0.1×100 = 11
Solution: write buffer
  Holds data waiting to be written to memory
  CPU continues immediately
    Only stalls on write if write buffer is already full

## Slide 29: Write-Back
Alternative: On data-write hit, just update the block in cache
  Keep track of whether each block is dirty
When a dirty block is replaced
  Write it back to memory
  Can use a write buffer to allow replacing block to be read first

## Slide 30: Write Allocation
What should happen on a write miss?
Alternatives for write-through
  Allocate on miss: fetch the block
  Write around: don’t fetch the block
    Since programs often write a whole block before reading it (e.g., initialization)
For write-back
  Usually fetch the block

## Slide 31: Multilevel Caches
Primary cache attached to CPU
  Small, but fast
Level-2 cache services misses from primary cache
  Larger, slower, but still faster than main memory
Main memory services L-2 cache misses
Some high-end systems include L-3 cache

## Slide 32: Measuring Cache Performance
Components of CPU time
  Program execution cycles
    Includes cache hit time
  Memory stall cycles
    Mainly from cache misses
With simplifying assumptions:
Memory Accesses
Program
× Miss Rate × Miss Penalty
Memory Stall Cycles =
Instructions
Program
Misses
Instructions
× Miss Penalty
×
=

## Slide 33: Cache Performance Example
Given
  I-cache miss rate = 2%
  D-cache miss rate = 4%
  Miss penalty = 100 cycles
  Base CPI (ideal cache) = 2
  Load & stores are 36% of instructions
Miss cycles per instruction
  I-cache: 0.02 × 100 = 2
  D-cache: 0.36 × 0.04 × 100 = 1.44
Actual CPI = 2 + 2 + 1.44 = 5.44
  Ideal CPU is 5.44/2 =2.72 times faster

## Slide 34: Average Access Time
Hit time is also important for performance
Average memory access time (AMAT)
  AMAT = Hit time + Miss rate × Miss penalty
Example
  CPU with 1ns clock, hit time = 1 cycle, miss penalty = 20 cycles, I-cache miss rate = 5%
  AMAT = 1 + 0.05 × 20 = 2ns
    2 cycles per instruction

## Slide 35: Overal Performance Summary
When CPU performance increased
  Miss penalty becomes more significant
Decreasing base CPI
  Greater proportion of time spent on memory stalls
Increasing clock rate
  Memory stalls account for more CPU cycles
Can’t neglect cache behavior when evaluating system performance

## Slide 36: Example: How Caches Affect Performance
Matrix Multiplication
Loop order: i, j, k
for (int i= 0; i < n; i++) { for (int j= 0; j < n; j++) { for (int k= 0; k < n; k++) { C[i][j]+= A[i][k]*B[k][j]; } } }
Loop order: i, k, j
for (int i= 0; i < n; i++) { for (int k= 0; k < n; k++) { for (int j= 0; j < n; j++) { C[i][j]+= A[i][k]*B[k][j]; } } }
Loop order: j, k, i
for (int j= 0; j < n; j++) { for (int k= 0; k < n; k++) { for (int i= 0; i < n; i++) { C[i][j]+= A[i][k]*B[k][j]; } } }
Running time:
13.714264 sec.
Performance:
~ 153 MFLOPS
Running time:
2.739385 sec.
Performance:
~ 795 MFLOPS
Running time:
19.074106 sec.
Performance:
~ 113 MFLOPS

## Slide 37: Memory Access Patterns
Loop order: i, j, k
Loop order: j, k, i
Loop order: i, k, j
A
A
A
B
B
B
C
C
C

## Slide 38: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero