## Slide 1: Computer Architecture and Operating Systems Lecture 3: Computer Architecture
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Computer Under Cover
Monitor
Hard drive
CPU (Processor)
Fan with cover
Spot for memory DIMMs
Spot for battery
Motherboard
Fan with cover
DVD drive
Keyboard
1 2 3 4 5 6 7 8 9 10

## Slide 3: Computer Organization
One or more CPUs and device controllers connected through a bus providing access to shared memory

## Slide 4: Program Under Hood
Application software
  Written in high-level language
System software
  Compiler: translates high-level language code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  CPU, memory, I/O controllers

## Slide 5: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 6: Abstractions
Abstraction helps us deal with complexity
  Hide lower-level detail
Instruction set architecture (ISA)
  The hardware/software interface
Application binary interface (ABI)
  The ISA plus system software interface
Implementation (microarchitecture)
  The details underlying the interface
Focus
of this course

## Slide 7: Inside the Processor (CPU)
Central Processing Unit (CPU) is the heart of any computer system.
Main components:
Register file: small fast memory for immediate access to data
Datapath: performs operations on data
Control unit: sequences datapath, memory, etc.

## Slide 8: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock period: duration of a clock cycle
  e.g., 250 ps = 0.25 ns = 250×10–12 s
Clock frequency (rate): cycles per second
  e.g., 4.0 GHz = 4000 MHz = 4.0×109 Hz
Clock (cycles)
Data transfer and computation
Update state
Clock period

## Slide 9: CPU Time
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc

## Slide 10: Instruction Set Architecture (ISA)
Instruction set architecture (ISA) is the interface between the hardware and the lowest-level software. This is one of the most important abstractions.
ISA Classification
Complex instruction set computer (CISC)
  x86/x64 (Intel and AMD)
Reduced instruction set computer (RISC)
  ARM, PowerPC, MIPS, RISC-V
Very long instruction word (VLIW)
  Itanium, Elbrus

## Slide 11: Reduced Instruction Set Computing (RISC)
Reduced Instruction Set Computing (RISC) concept was proposed by teams of researchers at Stanford University (John Hennessy) and University of California Berkeley (David Paterson) in early 1980s as an alternative of Complex Instruction Set Computing (CISC) dominating at that time.
RISC Principles
All instructions are executed by hardware
Maximize the rate at which instructions are issued
Instructions should be easy to decode
Only loads and stores should reference memory
Provide plenty of registers

## Slide 12: RISC-V ISA
Industry
Education
Research
Simple ISA by UC Berkeley (2010)
Open and Free
Wide-Purpose Configurable ISA (from IoT to mainframes)
Maintained by RISC-V Foundation (moved to Switzerland)
Supported by many IT Companies and Universities
Innovation

## Slide 13: RISC-V Community
and many others…
Wide Support of IT Companies (except Intel and ARM) and Universities

## Slide 14: Instruction Execution
Fetch next instruction from memory into instruction register
Change program counter to point to next instruction
Determine type of instruction just fetched
If instructions uses word in memory, determine where Fetch word, if needed, into CPU register
Execute the instruction
Go to step 1 to begin executing following instruction

## Slide 15: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero