## Slide 1: Computer Architecture and Operating Systems Lecture 10: Processor. Multiple Issue. Exceptions.
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Instruction-Level Parallelism (ILP)
Pipelining: executing multiple instructions in parallel
To increase ILP
  Deeper pipeline
    Less work per stage  shorter clock cycle
  Multiple issue
    Replicate pipeline stages  multiple pipelines
    Start multiple instructions per clock cycle
    CPI < 1, so use Instructions Per Cycle (IPC)
    E.g., 4GHz 4-way multiple-issue
      16 BIPS, peak CPI = 0.25, peak IPC = 4
    But dependencies reduce this in practice

## Slide 3: Multiple Issue
Static multiple issue
  Compiler groups instructions to be issued together
  Packages them into “issue slots”
  Compiler detects and avoids hazards
Dynamic multiple issue
  CPU examines instruction stream and chooses instructions to issue each cycle
  Compiler can help by reordering instructions
  CPU resolves hazards using advanced techniques at runtime

## Slide 4: Speculation
“Guess” what to do with an instruction
  Start operation as soon as possible
  Check whether guess was right
    If so, complete the operation
    If not, roll-back and do the right thing
Common to static and dynamic multiple issue
Examples
  Speculate on branch outcome
    Roll back if path taken is different
  Speculate on load
    Roll back if location is updated

## Slide 5: Compiler/Hardware Speculation
Compiler can reorder instructions
  e.g., move load before branch
  Can include “fix-up” instructions to recover from incorrect guess
Hardware can look ahead for instructions to execute
  Buffer results until it determines they are actually needed
  Flush buffers on incorrect speculation

## Slide 6: Static Multiple Issue
Compiler groups instructions into “issue packets”
  Group of instructions that can be issued on a single cycle
  Determined by pipeline resources required
Think of an issue packet as a very long instruction
  Specifies multiple concurrent operations
   Very Long Instruction Word (VLIW)

## Slide 7: Scheduling Static Multiple Issue
Compiler must remove some/all hazards
  Reorder instructions into issue packets
  No dependencies with a packet
  Possibly some dependencies between packets
    Varies between ISAs; compiler must know!
  Pad with nop if necessary

## Slide 8: RISC-V with Static Dual Issue
Two-issue packets
  One ALU/branch instruction
  One load/store instruction
  64-bit aligned
    ALU/branch, then load/store
    Pad an unused instruction with nop
Address | Instruction type | Pipeline Stages |  |  |  |  |  | 
n | ALU/branch | IF | ID | EX | MEM | WB |  | 
n + 4 | Load/store | IF | ID | EX | MEM | WB |  | 
n + 8 | ALU/branch |  | IF | ID | EX | MEM | WB | 
n + 12 | Load/store |  | IF | ID | EX | MEM | WB | 
n + 16 | ALU/branch |  |  | IF | ID | EX | MEM | WB
n + 20 | Load/store |  |  | IF | ID | EX | MEM | WB

## Slide 9: Dynamic Multiple Issue
“Superscalar” processors
CPU decides whether to issue 0, 1, 2, … each cycle
  Avoiding structural and data hazards
Avoids the need for compiler scheduling
  Though it may still help
  Code semantics ensured by the CPU

## Slide 10: Dynamic Pipeline Scheduling
Allow the CPU to execute instructions out of order to avoid stalls
  But commit result to registers in order
Example
  ld x31,20(x21) add x1,x31,x2 sub x23,x23,x3 andi x5,x23,20
  Can start sub while add is waiting for ld

## Slide 11: Why Do Dynamic Scheduling?
Why not just let the compiler schedule code?
Not all stalls are predicable
  e.g., cache misses
Can’t always schedule around branches
  Branch outcome is dynamically determined
Different implementations of an ISA have different latencies and hazards

## Slide 12: Dynamically Scheduled CPU
Results also sent to any waiting reservation stations
Reorders buffer for register writes
Can supply operands for issued instructions
Preserves dependencies
Hold pending operands

## Slide 13: Does Multiple Issue Work?
Yes, but not as much as we’d like
Programs have real dependencies that limit ILP
Some dependencies are hard to eliminate
  e.g., pointer aliasing
Some parallelism is hard to expose
  Limited window size during instruction issue
Memory delays and limited bandwidth
  Hard to keep pipelines full
Speculation can help if done well

## Slide 14: Conclusion
ISA influences design of datapath and control
Datapath and control influence design of ISA
Pipelining improves instruction throughput using parallelism
  More instructions completed per second
  Latency for each instruction not reduced
Hazards: structural, data, control
Multiple issue and dynamic scheduling (ILP)
  Dependencies limit achievable parallelism
  Complexity leads to the power wall

## Slide 15: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero