## Slide 1: Computer Architecture and Operating Systems Lecture 14: Thread-level parallelism
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Thread-Level Parallelism
Goal: connecting multiple computers to get higher performance
  Multiprocessors
  Scalability, availability, power efficiency
Task-level (process-level) parallelism
  High throughput for independent jobs
Parallel processing program
  Single program run on multiple processors
Multicore microprocessors
  Chips with multiple processors (cores)

## Slide 3: Parallel Programming
Parallel software is the problem
Need to get significant performance improvement
  Otherwise, just use a faster uniprocessor, since it’s easier!
Difficulties
  Partitioning
  Coordination
  Communications overhead

## Slide 4: Threads in Conventional Processor
One thread runs at once
When one thread stalls (for example, waiting for memory):
  Architectural state of that thread stored
  Architectural state of waiting thread loaded into processor and it runs
  Called context switching
Appears to user like all threads running simultaneously

## Slide 5: Multithreading
Multiple copies of architectural state
Multiple threads active at once:
  When one thread stalls, another runs immediately
  If one thread can’t keep all execution units busy, another thread can use them
Does not increase instruction-level parallelism (ILP) of single thread, but increases throughput
Intel calls this “hyperthreading”

## Slide 6: Multiprocessors
Multiple processors (cores) with a method of communication between them
Types:
  Homogeneous: multiple cores with shared memory
  Heterogeneous: separate cores for different tasks (for example, DSP and CPU in cell phone)
  Clusters: each core has own memory system

## Slide 7: Amdahl’s Law
Sequential part can limit speedup
Example: 100 processors, 90 × speedup?
  Tnew = Tparallelizable/100 + Tsequential
  Speedup =
  Solving: Fparallelizable = 0.999
Need sequential part to be 0.1% of original time

## Slide 8: Scaling Example 1
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors
Single processor: Time = (10 + 100) × tadd
10 processors
  Time = 10 × tadd + 100/10 × tadd = 20 × tadd
  Speedup = 110/20 = 5.5 (55% of potential)
100 processors
  Time = 10 × tadd + 100/100 × tadd = 11 × tadd
  Speedup = 110/11 = 10 (10% of potential)
Assumes load can be balanced across processors

## Slide 9: Scaling Example 2
What if matrix size is 100 × 100?
Single processor: Time = (10 + 10000) × tadd
10 processors
  Time = 10 × tadd + 10000/10 × tadd = 1010 × tadd
  Speedup = 10010/1010 = 9.9 (99% of potential)
100 processors
  Time = 10 × tadd + 10000/100 × tadd = 110 × tadd
  Speedup = 10010/110 = 91 (91% of potential)
Assuming load balanced

## Slide 10: Strong vs Weak Scaling
Strong scaling: problem size fixed
  As in example
Weak scaling: problem size proportional to number of processors
  10 processors, 10 × 10 matrix
    Time = 20 × tadd
  100 processors, 32 × 32 matrix
    Time = 10 × tadd + 1000/100 × tadd = 20 × tadd
  Constant performance in this example

## Slide 11: Threading: Definitions
Process: program running on a computer
  Multiple processes can run at once: e.g., surfing Web, playing music, writing a paper
Thread: part of a program
  Each process has multiple threads: e.g., a word processor may have threads for typing, spell checking, printing

## Slide 12: Multithreading
Performing multiple threads of execution in parallel
  Replicate registers, PC, etc.
  Fast switching between threads
Fine-grain multithreading
  Switch threads after each cycle
  Interleave instruction execution
  If one thread stalls, others are executed
Coarse-grain multithreading
  Only switch on long stall (e.g., L2-cache miss)
  Simplifies hardware, but doesn’t hide short stalls (eg, data hazards)

## Slide 13: Simultaneous Multithreading
In multiple-issue dynamically scheduled processor
  Schedule instructions from multiple threads
  Instructions from independent threads execute when function units are available
  Within threads, dependencies handled by scheduling and register renaming
Example: Intel Pentium-4 HT
  Two threads: duplicated registers, shared function units and caches

## Slide 14: Shared Memory
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform) vs. NUMA (nonuniform)

## Slide 15: Multithreading Example

## Slide 16: Message Passing
Each processor has private physical address space
Hardware sends/receives messages between processors

## Slide 17: Synchronization: Basic Building Blocks
Atomic exchange
  Swaps register with memory location
Test-and-set
  Sets under condition
Fetch-and-increment
  Reads original value from memory and increments it in memory
Requires read and write in uninterruptable instruction
RISC-V: load reserved/store conditional
  If the memory location specified by the load is changed before the store conditional to the same address, the store conditional fails

## Slide 18: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero