## Slide 1: Computer Architecture and Operating Systems Lecture 5: Assembly Programming – Branches and Arrays
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Program Structure and Memory Layout
Stack
Dynamic Data
.data
.text
Reserved
0x 0040 0000
0x 0000 0000
0x 1001 0000
0x 7FFF EFFC
.data
hello:
.string "Hello, world!"
.text
main:
li a7, 4
la a0, hello
ecall
0x1004 0000

## Slide 3: Labels
Labels are symbolic names for addresses (in the .data or .text segment).
Labels are used by control-flow instructions (branches and jumps).
Labels are used by load and store instructions.

## Slide 4: Addressing
Addresses can be represented in several ways

## Slide 5: Program Counter
Program Counter (PC) is a special register that stores the address of the currently executed instruction.
When an instruction is executed, the PC is incremented by the size of the instruction (4 bytes) to point to the next instruction.
Branch and jump instructions assign to the PC new addresses to change the control flow.
Branch instructions use PC-relative addresses (increment or decrement current value by an offset).

## Slide 6: Branch Instructions
Branch Instructions
Branch = beq rs1, rs2, label
Branch ≠ bne rs1, rs2, label
Branch < blt rs1, rs2, label
Branch ≥ bge rs1, rs2, label
Branch < Unsigned bltu rs1, rs2, label
Branch ≥ Unsigned bgeu rs1, rs2, label

## Slide 7: Branch Pseudoinstructions
Branch Pseudoinstructions
Branch unconditionally b label
Branch = 0 beqz rs1, label
Branch ≥ 0 bgez rs1, label
Branch > bgt rs1, rs2, label
Branch > Unsigned bgtu rs1, rs2, label
Branch > 0 bgtz rs1, label
Branch ≤ ble rs1, rs2, label
Branch ≤ Unsigned bleu rs1, rs2, label
Branch ≤ 0 blez rs1, label
Branch < 0 bltz rs1, label
Branch ≠ 0 bnez rs1, label

## Slide 8: Branches and Program Counter
Branch instructions are PC-relative
They add a 12-bit signed immediate to PC
The immediate is an offset from PC to the target label
The branch address range is ± 212 (4096 B = 4 KB)
PC can be read with the auipc instruction
main:
auipc a0, 0 # a0 = PC + 0
li a7, 34 # Print as hex
ecall # Print a0

## Slide 9: Assembly Code for “If-Then-Else”
if (t0 == 0) {
t1 = 1;
} else if (t0 < 0) {
t1 = 2;
} else if (t0 >= 10) {
t1 = 3;
} else {
t1 = 4;
}
if_0:
bnez t0, if_less_0
li t1, 1
b end_if
if_less_0:
bgtz t0, if_greater_10
li t1, 2
b end_if
if_greater_10:
li t3, 10
ble t0, t3, else
li t1, 3
b end_if
else:
li t1, 4
end_if:

## Slide 10: Assembly Code for “While”
while((t0 = read_int()) != 0) {
print_int(t0)
print_char('\n')
}
while:
li a7, 5
ecall
mv t0, a0
beqz a0, end_while
li a7, 1
ecall
li a7, 11
li a0, '\n'
ecall
b while
end_while:

## Slide 11: Assembly Code for “For”
for (t0 = 0; t0 < t1; ++t0) {
print_int(t0)
print_char('\n')
}
for:
li a7, 5
ecall
mv t1, a0
mv t0, zero
next:
beq t0, t1, end_for
mv a0, t0
li a7, 1
ecall
li a7, 11
li a0, '\n'
ecall
addi t0, t0, 1
b next
end_for:

## Slide 12: Assembly Code for Nested “For”
for (t0 = 0; t0 < s0; ++t0) {
for (t1 = 0; t0 < s1; ++t1) {
print_int(t0)
print_char(':')
print_int(t1)
print_int(' ')
}
print_char('\n')
}
mv t0, zero
next_t0:
beq t0, s0, end_for_t0
mv t1, zero
next_t1:
beq t1, s1, end_for_t1
print_int(t0)
print_char(':')
print_int(t1)
print_char(' ')
addi t1, t1, 1
b next_t1
end_for_t1:
print_char('\n')
addi t0, t0, 1
b next_t0
end_for_t0:

## Slide 13: Macros
Macro is a pattern-matching and replacement facility that provides a simple mechanism to name a frequently used sequence of instructions.
.macro print_int (%x)
li a7, 1
mv a0, %x
ecall
.end_macro
.macro read_int (%x)
li a7, 5
ecall
mv %x, a0
.end_macro
main:
read_int(t0)
print_int(t0)
Use Macros to Simplify Your Code

## Slide 14: Including Macro Libraries
It is possible to place macros in a library file and include it in other assembly programs.
The read_int and print_int macros are defined in the macrolib.s file.
The file must be in the same directory as the program.
.include "macrolib.s"
main:
read_int(t0)
print_int(t0)

## Slide 15: Macro Constants and Single-Line Macros
.eqv VAL 0x123
.eqv X t0
.eqv Y t1
.eqv SUM addi Y, X, VAL
main:
li X, 0x111
SUM
The .eqv directive can be used to define macro constants and single-line macros.

## Slide 16: Data Segment
Segment .data stores static data (global variables and constants), which are described with the following directives:
.data
.word 0xDEADBEEF # 32-bit value
.half 0x1234, 0x4567 # 16-bit values
.byte 0x98, 0x76, 0x65, 0x43 # 8-bit values
.space 8 # 8 bytes of empty space
.ascii "Hello " # String
.asciz "World! " # Zero-terminated string

## Slide 17: Data Alignment
Data items are aligned in memory by their size for convenience of access. This means address is multiple of size. Default alignment is as follows:
.byte # 1 byte
.half # 2 bytes
.word # 4 bytes
It is possible to specify a custom alignment by 2n bytes for a next data item with the .align directive.
.align 0 # 1 byte
.align 1 # 2 bytes
.align 2 # 4 bytes
.align 3 # 8 bytes
etc.

## Slide 18: Data Alignment Example
.data
.space 3
word1:
.word 0x12345678
half1:
.half 0x1234
byte1:
.byte 0x12
.align 4
word2:
.word 0x12345678
.align 3
half2:
.half 0x1234
.align 3
byte2:
.byte 0x12
.align 0
word3:
.word 0x12345678
Default
Alignment
Custom
Alignment

## Slide 19: Load and Store Instructions

## Slide 20: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero