## Slide 1: Computer Architecture and Operating Systems Lecture 11: Memory and Caches
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Processor-Memory Performance Gap
Computer performance depends on:
  Processor performance
  Memory performance

## Slide 3: Memory Challenge
Make memory appear as fast as processor
Ideal memory:
  Fast
  Cheap (inexpensive)
  Large (capacity)
But can only choose two!

## Slide 4: Memory Technology
Static RAM (SRAM)
  0.5ns – 2.5ns, $2000 – $5000 per GB
Dynamic RAM (DRAM)
  50ns – 70ns, $20 – $75 per GB
Magnetic disk
  5ms – 20ms, $0.20 – $2 per GB
Ideal memory
  Access time of SRAM
  Capacity and cost/GB of disk

## Slide 5: Locality
No need for large memory to access it fast
Just exploit locality
Temporal Locality:
  Locality in time
  If data used recently, likely to use it again soon
  How to exploit: keep recently accessed data in higher levels of memory hierarchy
Spatial Locality:
  Locality in space
  If data used recently, likely to use nearby data soon
  How to exploit: when access data, bring nearby data into higher levels of memory hierarchy too

## Slide 6: Taking Advantage of Locality
Memory hierarchy
Store everything on disk
Copy recently accessed (and nearby) items from disk to smaller DRAM memory
  Main memory
Copy more recently accessed (and nearby) items from DRAM to smaller SRAM memory
  Cache memory attached to CPU

## Slide 7: Memory Hierarchy
Personal mobile device
Laptop or desktop
Server

## Slide 8: How it works?
Block (aka line): unit of copying
  May be multiple words
If accessed data is present in upper level
  Hit: access satisfied by upper level
    Hit ratio: hits/accesses
If accessed data is absent
  Miss: block copied from lower level
    Time taken: miss penalty
    Miss ratio: misses/accesses = 1 – hit ratio
  Then accessed data supplied from upper level
Processor
L1
L2
Memory

## Slide 9: Memory Performance
Hit: data found in that level of memory hierarchy
Miss: data not found (must go to next level)
  Hit Rate = # hits / # memory accesses = 1 – Miss Rate
  Miss Rate = # misses / # memory accesses = 1 – Hit Rate
Average memory access time (AMAT): average time for processor to access data
  AMAT = tcache + MRcache[tMM + MRMM(tVM)]

## Slide 10: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero