## Slide 1: Computer Architecture and Operating Systems Lecture 4: Instruction Set Architecture
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: RISC-V ISA Base and Extensions
Name | Description | Version | Status
Base |  |  | 
RVWMO | Weak Memory Ordering | 2.0 | Ratified
RV32I | Base Integer Instruction Set, 32-bit | 2.1 | Ratified
RV64I | Base Integer Instruction Set, 64-bit | 2.1 | Ratified
RV128I | Base Integer Instruction Set, 128-bit | 1.7 | Open
Extensions |  |  | 
M | Standard Extension for Integer Multiplication and Division | 2.0 | Ratified
A | Standard Extension for Atomic Instructions | 2.1 | Ratified
F | Standard Extension for Single-Precision Floating-Point | 2.2 | Ratified
D | Standard Extension for Double-Precision Floating-Point | 2.2 | Ratified
G | Shorthand for the base integer set (I) and above extensions (MAFD) | N/A | N/A
Q | Standard Extension for Quad-Precision Floating-Point | 2.2 | Ratified
C | Standard Extension for Compressed Instructions | 2.0 | Ratified
ZiCSR | Control and Status Register (CSR) | 2.0 | Ratified
Zifencei | Instruction-Fetch Fence | 2.0 | Ratified
And more standard and custom extensions… |  |  | 

## Slide 3: ISA Design Principles
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
Design Principle 2: Smaller is faster
  c.f. main memory: millions of locations
Design Principle 3: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible

## Slide 4: Six Instruction Formats
R-format: instructions using 3 register inputs
  add, xor, mul - arithmetic/logical ops
I-format: instructions with immediates, loads
  addi, lw, jalr, slli
S-format: store instructions
  sw, sb
SB-format: branch instructions
  beq, bge
U-format: instructions with upper immediates
  lui, auipc - upper immediate is 20-bits
UJ-format: the jump instruction
  jal

## Slide 5: R-format Instructions
Arithmetic Instructions
  opcode: operation code
  rd: destination register number
  funct3: 3-bit function code (additional opcode)
  rs1 and rs2: first and second source register 5-bit numbers
  funct7: 7-bit function code (additional opcode)
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
add x9, x20, x21
0000 0001 0101 1010 0000 0100 1011 0011two = 015A04B316
0
21
20
9
0
51
0000000
10101
10100
01001
000
0110011

## Slide 6: I-format Instructions
Immediate arithmetic and load instructions
  rs1: source or base address register number
  immediate: constant operand, or offset added to base address
    2s-complement, sign extended
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits
0x123
6
5
0
19
000100100011
00110
00101
000
0010011
addi t0, t1, 123
0001 0010 0011 0011 0000 0010 1001 0011two = 0x1233029316

## Slide 7: S-format Instructions
Different immediate format for store instructions
  rs1: base address register number
  rs2: source operand register number
  immediate: offset added to base address
    Split so that rs1 and rs2 fields always in the same place
imm[11:5]
rs2
rs1
imm[4:0]
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
0
5
6
4
2
35
0000000
00101
00110
00100
010
100011
sw t0, 4(t1)
0000 0000 0101 0011 0010 0010 0010 0011two = 0x0053222316

## Slide 8: SB-format Instructions

## Slide 9: UJ-format Instructions

## Slide 10: U-format Instructions

## Slide 11: RISC-V Addressing Summary

## Slide 12: RISC-V Encoding Summary

## Slide 13: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero