## Slide 1: Computer Architecture and Operating Systems Lecture 7: Floating-Point Format
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Floating-Point Format
Representation for non-integral numbers
  Including very small and very large numbers
Like scientific notation
  –2.34 × 1056
  +0.002 × 10–4
  +987.02 × 109
In binary
  ±1.xxxxxxx2 × 2yyyy
Types float and double in C
normalized
not normalized

## Slide 3: Floating-Point Standard
Defined by IEEE Std 754-1985
Developed in response to divergence of representations
  Portability issues for scientific code
Now almost universally adopted
Two representations
  Single precision (32-bit)
  Double precision (64-bit)

## Slide 4: IEEE Floating-Point Format
S: sign bit (0  non-negative, 1  negative)
Normalized significand: 1.0 ≤ |significand| < 2.0
  Always has a leading pre-binary-point 1 bit, so no need to represent it explicitly (hidden bit)
  Significand is Fraction with the “1.” restored
Exponent: excess representation: actual exponent + Bias
  Ensures exponent is unsigned
  Single: Bias = 127; Double: Bias = 1203
S
Exponent
Fraction
single: 8 bits double: 11 bits
single: 23 bits double: 52 bits

## Slide 5: Single-Precision Range
Exponents 00000000 and 11111111 reserved
Smallest value
  Exponent: 00000001  actual exponent = 1 – 127 = –126
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–126 ≈ ±1.2 × 10–38
Largest value
  exponent: 11111110  actual exponent = 254 – 127 = +127
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+127 ≈ ±3.4 × 10+38

## Slide 6: Double-Precision Range
Exponents 0000…00 and 1111…11 reserved
Smallest value
  Exponent: 00000000001  actual exponent = 1 – 1023 = –1022
  Fraction: 000…00  significand = 1.0
  ±1.0 × 2–1022 ≈ ±2.2 × 10–308
Largest value
  Exponent: 11111111110  actual exponent = 2046 – 1023 = +1023
  Fraction: 111…11  significand ≈ 2.0
  ±2.0 × 2+1023 ≈ ±1.8 × 10+308

## Slide 7: Floating-Point Precision
Relative precision
  all fraction bits are significant
  Single: approx 2–23
    Equivalent to 23 × log102 ≈ 23 × 0.3 ≈ 6 decimal digits of precision
  Double: approx 2–52
    Equivalent to 52 × log102 ≈ 52 × 0.3 ≈ 16 decimal digits of precision

## Slide 8: Floating-Point Example
Represent –0.75
  –0.75 = (–1)1 × 1.12 × 2–1
  S = 1
  Fraction = 1000…002
  Exponent = –1 + Bias
    Single: –1 + 127 = 126 = 011111102
    Double: –1 + 1023 = 1022 = 011111111102
Single: 1011111101000…00
Double: 1011111111101000…00

## Slide 9: Floating-Point Example
What number is represented by the single-precision float 11000000101000…00
  S = 1
  Fraction = 01000…002
  Fxponent = 100000012 = 129
x = (–1)1 × (1 + 012) × 2(129 – 127)
  = (–1) × 1.25 × 22
  = –5.0

## Slide 10: Denormal Numbers
Exponent = 000...0  hidden bit is 0
Two representations of 0.0!
Smaller than normal numbers
  allow for gradual underflow, with diminishing precision
Denormal with fraction = 000...0

## Slide 11: Infinities and NaNs
Exponent = 111...1, Fraction = 000...0
  ±Infinity
  Can be used in subsequent calculations, avoiding need for overflow check
Exponent = 111...1, Fraction ≠ 000...0
  Not-a-Number (NaN)
  Indicates illegal or undefined result
    e.g., 0.0 / 0.0
  Can be used in subsequent calculations

## Slide 12: Floating-Point Addition
Consider a 4-digit decimal example
  9.999 × 101 + 1.610 × 10–1
1. Align decimal points
  Shift number with smaller exponent
  9.999 × 101 + 0.016 × 101
2. Add significands
  9.999 × 101 + 0.016 × 101 = 10.015 × 101
3. Normalize result & check for over/underflow
  1.0015 × 102
4. Round and renormalize if necessary
  1.002 × 102

## Slide 13: Floating-Point Addition
Now consider a 4-digit binary example
  1.0002 × 2–1 + –1.1102 × 2–2 (0.5 + –0.4375)
1. Align binary points
  Shift number with smaller exponent
  1.0002 × 2–1 + –0.1112 × 2–1
2. Add significands
  1.0002 × 2–1 + –0.1112 × 2–1 = 0.0012 × 2–1
3. Normalize result & check for over/underflow
  1.0002 × 2–4, with no over/underflow
4. Round and renormalize if necessary
  1.0002 × 2–4 (no change) = 0.0625

## Slide 14: FP Adder Hardware
Much more complex than integer adder
Doing it in one clock cycle would take too long
  Much longer than integer operations
  Slower clock would penalize all instructions
FP adder usually takes several cycles
  Can be pipelined

## Slide 15: FP Adder Hardware
Step 1
Step 2
Step 3
Step 4

## Slide 16: Floating-Point Multiplication
Consider a 4-digit decimal example
  1.110 × 1010 × 9.200 × 10–5
1. Add exponents
  For biased exponents, subtract bias from sum
  New exponent = 10 + –5 = 5
2. Multiply significands
  1.110 × 9.200 = 10.212  10.212 × 105
3. Normalize result & check for over/underflow
  1.0212 × 106
4. Round and renormalize if necessary
  1.021 × 106
5. Determine sign of result from signs of operands
  +1.021 × 106

## Slide 17: Floating-Point Multiplication
Now consider a 4-digit binary example
  1.0002 × 2–1 × –1.1102 × 2–2 (0.5 × –0.4375)
1. Add exponents
  Unbiased: –1 + –2 = –3
  Biased: (–1 + 127) + (–2 + 127) = –3 + 254 – 127 = –3 + 127
2. Multiply significands
  1.0002 × 1.1102 = 1.1102  1.1102 × 2–3
3. Normalize result & check for over/underflow
  1.1102 × 2–3 (no change) with no over/underflow
4. Round and renormalize if necessary
  1.1102 × 2–3 (no change)
5. Determine sign: +ve × –ve  –ve
  –1.1102 × 2–3 = –0.21875

## Slide 18: FP Arithmetic Hardware
FP multiplier is of similar complexity to FP adder
  But uses a multiplier for significands instead of an adder
FP arithmetic hardware usually does
  Addition, subtraction, multiplication, division, reciprocal, square-root
  FP  integer conversion
Operations usually takes several cycles
  Can be pipelined

## Slide 19: FP Instructions in RISC-V
Separate FP registers: f0, …, f31
  double-precision
  single-precision values stored in the lower 32 bits
FP instructions operate only on FP registers
  Programs generally don’t do integer ops on FP data, or vice versa
  More registers with minimal code-size impact
FP load and store instructions
  flw, fld
  fsw, fsd

## Slide 20: FP Instructions in RISC-V
Single-precision arithmetic
  fadd.s, fsub.s, fmul.s, fdiv.s, fsqrt.s
    e.g., fadds.s f2, f4, f6
Double-precision arithmetic
  fadd.d, fsub.d, fmul.d, fdiv.d, fsqrt.d
    e.g., fadd.d f2, f4, f6
Single- and double-precision comparison
  feq.s, flt.s, fle.s
  feq.d, flt.d, fle.d
  Result is 0 or 1 in integer destination register
    Use beq, bne to branch on comparison result
Branch on FP condition code true or false
  b.cond

## Slide 21: FP Example: °F to °C
C code:
float f2c (float fahr) { return ((5.0/9.0)*(fahr - 32.0)); }
  fahr in f10, result in f10, literals in global memory space
Compiled RISC-V code:
f2c:
flw f0,const5(x3) // f0 = 5.0f
flw f1,const9(x3) // f1 = 9.0f
fdiv.s f0, f0, f1 // f0 = 5.0f / 9.0f
flw f1,const32(x3) // f1 = 32.0f
fsub.s f10,f10,f1 // f10 = fahr – 32.0
fmul.s f10,f0,f10 // f10 = (5.0f/9.0f) * (fahr–32.0f)
jalr x0,0(x1) // return

## Slide 22: FP Example: Array Multiplication
C = C + A × B
  All 32 × 32 matrices, 64-bit double-precision elements
C code:
void mm (double c[][], double a[][], double b[][]) { size_t i, j, k; for (i = 0; i < 32; i = i + 1) for (j = 0; j < 32; j = j + 1) for (k = 0; k < 32; k = k + 1) c[i][j] = c[i][j] + a[i][k] * b[k][j]; }
  Addresses of c, a, b in x10, x11, x12, and i, j, k in x5, x6, x7

## Slide 23: FP Example: Array Multiplication
RISC-V code:
mm:...
li x28,32 // x28 = 32 (row size/loop end)
li x5,0 // i = 0; initialize 1st for loop
L1: li x6,0 // j = 0; initialize 2nd for loop
L2: li x7,0 // k = 0; initialize 3rd for loop
slli x30,x5,5 // x30 = i * 2**5 (size of row of c)
add x30,x30,x6 // x30 = i * size(row) + j
slli x30,x30,3 // x30 = byte offset of [i][j]
add x30,x10,x30 // x30 = byte address of c[i][j]
fld f0,0(x30) // f0 = c[i][j]
L3: slli x29,x7,5 // x29 = k * 2**5 (size of row of b)
add x29,x29,x6 // x29 = k * size(row) + j
slli x29,x29,3 // x29 = byte offset of [k][j]
add x29,x12,x29 // x29 = byte address of b[k][j]
fld f1,0(x29) // f1 = b[k][j]

## Slide 24: FP Example: Array Multiplication
…
slli x29,x5,5 // x29 = i * 2**5 (size of row of a)
add x29,x29,x7 // x29 = i * size(row) + k
slli x29,x29,3 // x29 = byte offset of [i][k]
add x29,x11,x29 // x29 = byte address of a[i][k]
fld f2,0(x29) // f2 = a[i][k]
fmul.d f1, f2, f1 // f1 = a[i][k] * b[k][j]
fadd.d f0, f0, f1 // f0 = c[i][j] + a[i][k] * b[k][j]
addi x7,x7,1 // k = k + 1
bltu x7,x28,L3 // if (k < 32) go to L3
fsd f0,0(x30) // c[i][j] = f0
addi x6,x6,1 // j = j + 1
bltu x6,x28,L2 // if (j < 32) go to L2
addi x5,x5,1 // i = i + 1
bltu x5,x28,L1 // if (i < 32) go to L1

## Slide 25: Accurate Arithmetic
IEEE Std 754 specifies additional rounding control
  Extra bits of precision (guard, round, sticky)
  Choice of rounding modes
  Allows programmer to fine-tune numerical behavior of a computation
Not all FP units implement all options
  Most programming languages and FP libraries just use defaults
Trade-off between hardware complexity, performance, and market requirements

## Slide 26: Associativity
Parallel programs may interleave operations in unexpected orders
  Assumptions of associativity may fail
Need to validate parallel programs under varying degrees of parallelism

## Slide 27: Who Cares About FP Accuracy?
Important for scientific code
  But for everyday consumer use?
    “My bank balance is out by 0.0002¢!” 
The Intel Pentium FDIV bug
  The market expects accuracy
  See Colwell, The Pentium Chronicles

## Slide 28: Concluding Remarks
Bits have no inherent meaning
  Interpretation depends on the instructions applied
Computer representations of numbers
  Finite range and precision
  Need to account for this in programs

## Slide 29: Concluding Remarks
ISAs support arithmetic
  Signed and unsigned integers
  Floating-point approximation to reals
Bounded range and precision
  Operations can overflow and underflow

## Slide 30: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero