## Slide 1: Computer Architecture and Operating Systems Lecture 2: Data Representation
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Everything is Bits
Each bit is 0 or 1
By encoding/interpreting sets of bits in various ways
  Computers determine what to do (instructions)
  … and represent and manipulate numbers, sets, strings, etc…
Why bits? Electronic implementation
  Easy to store with bistable elements
  Reliably transmitted on noisy and inaccurate wires
0.0V
0.2V
0.9V
1.1V
0
1
0

## Slide 3: Number Systems
Decimal numbers
Binary numbers

## Slide 4: Powers of Two
20 = 1
21 = 2
22 = 4
23 = 8
24 = 16
25 = 32
26 = 64
27 = 128
Handy to memorize up to 210
28 = 256
29 = 512
210 = 1024
211 = 2048
212 = 4096
213 = 8192
214 = 16384
215 = 32768

## Slide 5: Number Conversion
Decimal to binary conversion:
  Convert 100112 to decimal
  16×1 + 8×0 + 4×0 + 2×1 + 1×1 = 1910
Decimal to binary conversion:
  Convert 4710 to binary
  32×1 + 16×0 + 8×1 + 4×1 + 2×1 + 1×1 = 1011112

## Slide 6: Binary Values and Range
N-digit decimal number
  How many values? 10N
  Range? [0, 10N - 1]
  Example: 3-digit decimal number:
    103 = 1000 possible values
    Range: [0, 999]
N-bit binary number
  How many values? 2N
  Range: [0, 2N - 1]
  Example: 3-digit binary number:
    23 = 8 possible values
    Range: [0, 7] = [0002 to 1112]

## Slide 7: Hexadecimal Numbers
Base 16
Shorthand for binary
Hex Digit | Decimal Equivalent | Binary Equivalent
0 | 0 | 0000
1 | 1 | 0001
2 | 2 | 0010
3 | 3 | 0011
4 | 4 | 0100
5 | 5 | 0101
6 | 6 | 0110
7 | 7 | 0111
8 | 8 | 1000
9 | 9 | 1001
A | 10 | 1010
B | 11 | 1011
C | 12 | 1100
D | 13 | 1101
E | 14 | 1110
F | 15 | 1111

## Slide 8: Hexadecimal to Binary Conversion
Hexadecimal to binary conversion:
  Convert 4AF16 (also written 0x4AF) to binary
  0100 1010 11112
Hexadecimal to decimal conversion:
  Convert 4AF16 to decimal
  162×4 + 161×10 + 160×15 = 119910

## Slide 9: Bits, Bytes, Nibbles…
Bits
Bytes & Nibbles
Bytes

## Slide 10: Encoding Byte Values
Byte = 8 bits
  Binary 000000002 to 111111112
  Decimal: 010 to 25510
  Hexadecimal 0016 to FF16
    Base 16 number representation
    Use characters ‘0’ to ‘9’ and ‘A’ to ‘F’
    Write FA1D37B16 in C as
      0xFA1D37B
      0xfa1d37b

## Slide 11: Example Data Representations
C Data Type | Typical 32-bit | Typical 64-bit
char | 1 | 1
short | 2 | 2
int | 4 | 4
long | 4 | 8
float | 4 | 4
double | 8 | 8
long double | − | −
pointer | 4 | 8

## Slide 12: Byte-Oriented Memory Organization
Programs refer to data by address
  Conceptually, envision it as a very large array of bytes
    In reality, it’s not, but can think of it that way
  An address is like an index into that array
    and, a pointer variable stores an address
Note: system provides private address spaces to each “process”
  Think of a process as a program being executed
  So, a program can clobber its own data, but not that of others
• • •
00•••0
FF•••F

## Slide 13: Machine Words
Word is a native unit of information handled by computer
Any computer has a “Word Size”
  Nominal size of integer-valued data
    and of addresses
  Until recently, most machines used 32 bits (4 bytes) as word size
    Limits addresses to 4GB (232 bytes)
  Increasingly, machines have 64-bit word size
    Potentially, could have 18 EB (exabytes) of addressable memory
    That’s 18.4 X 1018
  Machines still support multiple data formats
    Fractions or multiples of word size
    Always integral number of bytes

## Slide 14: Word-Oriented Memory Organization
Addresses Specify Byte Locations
  Address of first byte in word
  Addresses of successive words differ by 4 (32-bit) or 8 (64-bit)
0000
0001
0002
0003
0004
0005
0006
0007
0008
0009
0010
0011
32-bit
Words
Bytes
Addr.
0012
0013
0014
0015
64-bit
Words
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
Addr
=
??
0000
0004
0008
0012
0000
0008

## Slide 15: Byte Ordering
How are the bytes within a multi-byte word ordered in memory?
Conventions
  Big Endian: Sun, PPC Mac, Internet
    Least significant byte has highest address
  Little Endian: x86, ARM processors running Android, iOS, and Windows, RISC-V
    Least significant byte has lowest address

## Slide 16: Byte Ordering Example
Example
  Variable x has 4-byte value of 0x01234567
  Address given by &x is 0x100
0x100
0x101
0x102
0x103
01
23
45
67
0x100
0x101
0x102
0x103
67
45
23
01
Big Endian
Little Endian
01
23
45
67
67
45
23
01

## Slide 17: Encoding Integers
Sign Bit
  For 2’s complement, most significant bit indicates sign
    0 for nonnegative
    1 for negative
Unsigned
Signed (two’s complement)
Sign Bit
 | Decimal | Hex | Binary
x | 15213 | 3B 6D | 00111011 01101101
y | -15213 | C4 93 | 11000100 10010011
C short 2 bytes long

## Slide 18: Two-complement Encoding Example
x = 15213: 00111011 01101101
y = -15213: 11000100 10010011
Weight | 15213 |  | -15213 | 
1 | 1 | 1 | 1 | 1
2 | 0 | 0 | 1 | 2
4 | 1 | 4 | 0 | 0
8 | 1 | 8 | 0 | 0
16 | 0 | 0 | 1 | 16
32 | 1 | 32 | 0 | 0
64 | 1 | 64 | 0 | 0
128 | 0 | 0 | 1 | 128
256 | 1 | 256 | 0 | 0
512 | 1 | 512 | 0 | 0
1024 | 0 | 0 | 1 | 1024
2048 | 1 | 2048 | 0 | 0
4096 | 1 | 4096 | 0 | 0
8192 | 1 | 8192 | 0 | 0
16384 | 0 | 0 | 1 | 16384
-32768 | 0 | 0 | 1 | -32768
Sum |  | 15213 |  | -15213

## Slide 19: Boolean Algebra
Developed by George Boole in 19th Century
  Algebraic representation of logic
    Encode “True” as 1 and “False” as 0
And
A&B = 1 when both A=1 and B=1
Or
A|B = 1 when either A=1 or B=1
Not
~A = 1 when A=0
Exclusive-Or (Xor)
A^B = 1 when either A=1 or B=1, but not both

## Slide 20: Bitwise Operations
Operate on Bit Vectors
  Operations applied bitwise
All of the Properties of Boolean Algebra Apply
01101001
& 01010101
01000001
01101001
| 01010101
01111101
01101001
^ 01010101
00111100
~ 01010101
10101010

## Slide 21: Logic Operations
  Operations &&, ||, !
  Different from similar bitwise operations
  View 0 as “False”
  Anything nonzero as “True”
  Always return 0 or 1
  Early termination
Examples (8-bit data type)
  !0x41 => 0x00
  !0x00 => 0x01
  !!0x41 => 0x01
  0x69 && 0x55 => 0x01
  0x69 || 0x55 => 0x01

## Slide 22: Sign-Extension
Extend number from N to M bits (M > N)
Sign bit is copied to most significant bits
Number value is same
Example 1:
  4-bit representation of 3 = 0011
  8-bit sign-extended value: 00000011
Example 2:
  4-bit representation of -5 = 1011
  8-bit sign-extended value: 11111011

## Slide 23: Zero-Extension
Extend number from N to M bits (M > N)
Zeros are copied to most significant bits
Value changes for negative numbers
Example 1:
  4-bit value = 0011 = 310
  8-bit zero-extended value: 00000011 = 310
Example 2:
  4-bit value = 1011 = -510
  8-bit zero-extended value: 00001011 = 1110

## Slide 24: Shift Operations
Left Shift: x << y
  Shift bit-vector x left y positions
    Throw away extra bits on left
  Fill with 0’s on right
Right Shift: x >> y
  Shift bit-vector x right y positions
    Throw away extra bits on right
  Logical shift
    Fill with 0’s on left
  Arithmetic shift
    Replicate most significant bit on left
Undefined Behavior
  Shift amount < 0 or ≥ word size
01100010
X
00010000
<< 3
00011000
Log. >> 2
00011000
Arith. >> 2
10100010
X
00010000
<< 3
00101000
Log. >> 2
11101000
Arith. >> 2
00010000
00010000
00011000
00011000
00011000
00011000
00010000
00101000
11101000
00010000
00101000
11101000

## Slide 25: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero