## Slide 1: Computer Architecture and Operating Systems Lecture 16: Domain-specific architectures. Tensor Processing Unit.
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Motivation
Modern performance tuning techniques:
  Deep memory hierarchy
  Wide SIMD units
  Deep pipelines
  Branch prediction
  Out-of-order execution
  Speculative prefetching
  Multithreading
  Multiprocessing
Further improvement:
  Domain-specific architectures

## Slide 3: Guidelines for DSAs
Use dedicated memories to minimize data movement
Invest resources into more arithmetic units or bigger memories
Use the easiest form of parallelism that matches the domain
Reduce data size and type to the simplest needed for the domain
Use a domain-specific programming language

## Slide 4: Deep Neural Networks
Inpired by neuron of the brain
Computes non-linear “activation” function of the weighted sum of input values
Neurons arranged in layers
Most practitioners will choose an existing design
  Topology
  Data type
Training (learning):
  Calculate weights using backpropagation algorithm
  Supervised learning: stochastic graduate descent
Inference: use neural network for classification

## Slide 5: Convolutional Neural Network
Batches:
  Reuse weights once fetched from memory across multiple inputs
  Increases operational intensity
Quantization
  Use 8- or 16-bit fixed point
Summary:
  Need the following kernels:
    Matrix-vector multiply
    Matrix-matrix multiply
    Stencil
    ReLU
    Sigmoid
    Hyperbolic tangeant

## Slide 6: Tensor Processing Unit
Google’s DNN ASIC
256 x 256 8-bit matrix multiply unit
Large software-managed scratchpad
Coprocessor on the PCIe bus

## Slide 7: Tensor Processing Unit

## Slide 8: TPU ISA
Read_Host_Memory
  Reads memory from the CPU memory into the unified buffer
Read_Weights
  Reads weights from the Weight Memory into the Weight FIFO as input to the Matrix Unit
MatrixMatrixMultiply/Convolve
  Perform a matrix-matrix multiply, a vector-matrix multiply, an element-wise matrix multiply, an element-wise vector multiply, or a convolution from the Unified Buffer into the accumulators
  takes a variable-sized B*256 input, multiplies it by a 256x256 constant input, and produces a B*256 output, taking B pipelined cycles to complete
Activate
  Computes activation function
Write_Host_Memory
  Writes data from unified buffer into host memory

## Slide 9: Tensor Processing Unit

## Slide 10: TPU ISA

## Slide 11: The TPU and the Guidelines
Use dedicated memories
  24 MiB dedicated buffer, 4 MiB accumulator buffers
Invest resources in arithmetic units and dedicated memories
  60% of the memory and 250X the arithmetic units of a server-class CPU
Use the easiest form of parallelism that matches the domain
  Exploits 2D SIMD parallelism
Reduce the data size and type needed for the domain
  Primarily uses 8-bit integers
Use a domain-specific programming language
  Uses TensorFlow

## Slide 12: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero