## Slide 1: Computer Architecture and Operating Systems Lecture 3: Computer Architecture
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Computer Under Cover
Monitor
Hard drive
CPU (Processor)
Fan with cover
Spot for memory DIMMs
Spot for battery
Motherboard
Fan with cover
DVD drive
Keyboard
1 2 3 4 5 6 7 8 9 10

## Slide 3: Computer Organization
One or more CPUs and device controllers connected through a bus providing access to shared memory

## Slide 4: Program Under Hood
Application software
  Written in high-level language
System software
  Compiler: translates high-level language code to machine code
  Operating System: service code
    Handling input/output
    Managing memory and storage
    Scheduling tasks & sharing resources
Hardware
  CPU, memory, I/O controllers

## Slide 5: Levels of Program Code
High-level language
  Level of abstraction closer to problem domain
  Provides productivity and portability
Assembly language
  Textual representation of instructions
Hardware representation
  Binary digits (bits)
  Encoded instructions and data

## Slide 6: Abstractions
Abstraction helps us deal with complexity
  Hide lower-level detail
Instruction set architecture (ISA)
  The hardware/software interface
Application binary interface (ABI)
  The ISA plus system software interface
Implementation (microarchitecture)
  The details underlying the interface
Focus
of this course

## Slide 7: Inside the Processor (CPU)
Central Processing Unit (CPU) is the heart of any computer system.
Main components:
Register file: small fast memory for immediate access to data
Datapath: performs operations on data
Control unit: sequences datapath, memory, etc.

## Slide 8: CPU Clocking
Operation of digital hardware governed by a constant-rate clock
Clock period: duration of a clock cycle
  e.g., 250 ps = 0.25 ns = 250×10–12 s
Clock frequency (rate): cycles per second
  e.g., 4.0 GHz = 4000 MHz = 4.0×109 Hz
Clock (cycles)
Data transfer and computation
Update state
Clock period

## Slide 9: CPU Time
Performance depends on
  Algorithm: affects IC, possibly CPI
  Programming language: affects IC, CPI
  Compiler: affects IC, CPI
  Instruction set architecture: affects IC, CPI, Tc

## Slide 10: Instruction Set Architecture (ISA)
Instruction set architecture (ISA) is the interface between the hardware and the lowest-level software. This is one of the most important abstractions.
ISA Classification
Complex instruction set computer (CISC)
  x86/x64 (Intel and AMD)
Reduced instruction set computer (RISC)
  ARM, PowerPC, MIPS, RISC-V
Very long instruction word (VLIW)
  Itanium, Elbrus

## Slide 11: Reduced Instruction Set Computing (RISC)
Reduced Instruction Set Computing (RISC) concept was proposed by teams of researchers at Stanford University (John Hennessy) and University of California Berkeley (David Paterson) in early 1980s as an alternative of Complex Instruction Set Computing (CISC) dominating at that time.
RISC Principles
All instructions are executed by hardware
Maximize the rate at which instructions are issued
Instructions should be easy to decode
Only loads and stores should reference memory
Provide plenty of registers

## Slide 12: RISC-V ISA
Industry
Education
Research
Simple ISA by UC Berkeley (2010)
Open and Free
Wide-Purpose Configurable ISA (from IoT to mainframes)
Maintained by RISC-V Foundation (moved to Switzerland)
Supported by many IT Companies and Universities
Innovation

## Slide 13: RISC-V Community
and many others…
Wide Support of IT Companies (except Intel and ARM) and Universities

## Slide 14: How CPU Works
32 bit words
000000…000
32-bit words
ALU
Register File
Arithmetic
Logic Unit
x0
x1
x2
x3
…
x31
Machine language directly
reflects this structure
Main Memory
Stores program and data
0
4
8
12
16
20

## Slide 15: Instruction Execution
Fetch next instruction from memory into instruction register
Change program counter to point to next instruction
Determine type of instruction just fetched
If instructions uses word in memory, determine where Fetch word, if needed, into CPU register
Execute the instruction
Go to step 1 to begin executing following instruction

## Slide 16: RISC-V CPU Scheme

## Slide 17: RISC-V General-Purpose Registers
Register | Name | Use | Saver
x0 | zero | constant 0 | n/a
x1 | ra | return addr | caller
x2 | sp | stack ptr | callee
x3 | gp | gbl ptr | 
x4 | tp | thread ptr | 
x5-x7 | t0-t2 | temporaries | caller
x8 | s0/fp | saved/ frame ptr | callee
x9 | s1 | saved | callee
x10-x17 | a0-a7 | arguments | caller
x18-x27 | s2-s11 | saved | callee
x28-x31 | t3-t6 | temporaries | caller
32 Registers
32 (or 64) Bits Wide

## Slide 18: RISC-V Instructions
Fixed-size 32 bit instructions
Always three operands: d -> op(s, t)
Instruction types
  Computational instructions
  Load-store instructions
  Control-transfer instructions
  System instructions
All operations done with registers

## Slide 19: Assembly Programming
Primitive arithmetic and logical operations
Complex data types and data structures
Complex control structures – conditional statements, loops and procedures
Not suitable for direct implementation in hardware
Primitive arithmetic and logical operations
Primitive data structures – bits and integers
Control transfer instructions
Designed to be directly implementable in hardware
High Level Language vs Assembly Language
tedious programming!

## Slide 20: Computational Instructions
Arithmetic, comparison, logical, and shift operations.
Register-Register Instructions:
  2 source operand registers
  1 destination register
  Format: op dest, src1, src2
Arithmetic | Comparisons | Logical | Shifts
add, sub | slt, sltu | and, or, xor | sll, srl, sra
  add x3, x1, x2
  slt x3, x1, x2
  and x3, x1, x2
  sll x3, x1, x2
x3 <- x1 + x2
if x1 < x2 then x3 = 1 else x3 = 0
x3 <- x1 & x2
x3 <- x1 << x2

## Slide 21: Register-Immediate Instructions
One operand comes from a register and the other is a small constant that is encoded into the instruction.
  Format: op dest, src1, src2
Format | Arithmetic | Comparisons | Logical | Shifts
Register-Register | add, sub | slt, sltu | and, or, xor | sll, srl, sra
Register-Immediate | addi | slti, sltiu | andi, ori, xori | slli, srli, srai
addi x3, x1, 3
andi x3, x1, 3
slli x3, x1, 3
addi x3, x1, -3
x3 <- x1 + 3
x3 <- x1 & 3
x3 <- x1 << 3
x3 <- x1 - 3
No subi, instead use negative constant.

## Slide 22: Compound Computations
Execute a = ((b+3) >> c) - 1;
  Break up complex expression into basic computations.
    Our instructions can only specify two source operands and one destination operand (also known as three address instruction).
  Assume a, b, c are in registers x1, x2, and x3 respectively. Use x4 for t0, and x5 for t1.
t0 = b + 3;
t1 = t0 >> c;
a = t1 - 1;
addi x4, x2, 3
srl x5, x4, x3
addi x1, x5, -1

## Slide 23: Control Flow Instructions
Need Conditional branch instructions:
  Format: comp src1, src2, label
  First performs comparison to determine if branch is taken or not: src1 comp src2
  If comparison returns True, then branch is taken, else continue executing program in order.
if (a < b): c = a + 1
else: c = b + 2
assume
x1=a; x2=b; x3=c;
bge x1, x2, else
addi x3, x1, 1
beq x0, x0, end
else:
addi x3, x2, 2
end:

## Slide 24: Unconditional Control Instructions: Jumps
jal: Unconditional jump and link
  Example: jal x3, label
  Jump target specified as label
  label is encoded as an offset from current instruction
  Link (to be discussed later): is stored in x3
jalr: Unconditional jump via register and link
  Example: jalr x3, 4(x1)
  Jump target specified as register value plus constant offset
  Example: Jump target = x1 + 4
  Can jump to any 32 bit address – supports long jumps

## Slide 25: Constants and Instruction Encoding Limits
Instructions are encoded as 32 bits
  Need to specify operation (10 bits)
  Need to specify 2 source registers (10 bits) or 1 source register (5 bits) plus a small constant
  Need to specify 1 destination register (5 bits)
The constant in register-immediate instructions has to be smaller than 12 bits; bigger constants have to be stored in the memory or a register and then used explicitly
The constant in a jal instruction is 20 bits wide (7 bits for operation, and 5 bits for register)

## Slide 26: Computations on Values in Memory
b
c
a
32 bit words
Main Memory
0x0
0x4
0x8
0xC
0x10
0x14
a = b + c
x1 <- load(Mem[b])
x2 <- load(Mem[c])
x3 <- x1 + x2
store(Mem[a]) <- x3
x1 <- load(0x4)
x2 <- load(0x8)
x3 <- x1 + x2
store(0x10) <- x3

## Slide 27: Load and Store Instructions
Address is specified as a <base address, offset> pair:
  Base address is always stored in a register
  Offset is specified as a small constant
  Format: lw dest, offset(base) sw src, offset(base)
lw x1, 0x4(x0)
lw x2, 0x8(x0)
add x3, x1, x2
sw x3, 0x10(x0)
x1 <- load(Mem[x0 + 0x4])
x2 <- load(Mem[x0 + 0x8])
x3 <- x1 + x2
store(Mem[x0 + 0x10]) <- x3

## Slide 28: Pseudoinstructions
Aliases to other actual instructions to simplify assembly programming.
Pseudoinstruction:
mv x2, x1
li x2, 3
ble x1, x2, label
beqz x1, label
bnez x1, label
j label
Equivalent Assembly Instruction:
addi x2, x1, 0
addi x2, x0, 3
bge x2, x1, label
beq x1, x0, label
bne x1, x0, label
jal x0, label

## Slide 29: Example: Program to Sum Array Elements
Main Memory
sum = a[0] + a[1] + a[2] + ... + a[n-1]
(assume base address 100 is already in x10)
lw x1, 0x0(x10)
lw x2, 0x4(x10)
add x3, x0, x0
loop:
lw x4, 0x0(x1)
add x3, x3, x4
addi x1, x1, 4
addi x2, x2, -1
bnez x2, loop
sw x3, 0x8(x10)
a[0]
a[1]
a[n-1]
0
4
100
104
108
Addr of a[i]
n
sum
100
Register File
x1
x2
x3
x10
base
n
sum

## Slide 30: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero