## Slide 1: Computer Architecture and Operating Systems Lecture 5: Assembly Programming – Branches and Arrays
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Program Structure and Memory Layout
Stack
Dynamic Data
.data
.text
Reserved
0x 0040 0000
0x 0000 0000
0x 1001 0000
0x 7FFF EFFC
.data
hello:
.string "Hello, world!"
.text
main:
li a7, 4
la a0, hello
ecall
0x1004 0000

## Slide 3: Labels
Labels are symbolic names for addresses (in the .data or .text segment).
Labels are used by control-flow instructions (branches and jumps).
Labels are used by load and store instructions.

## Slide 4: Addressing
Addresses can be represented in several ways

## Slide 5: Program Counter
Program Counter (PC) is a special register that stores the address of the currently executed instruction.
When an instruction is executed, the PC is incremented by the size of the instruction (4 bytes) to point to the next instruction.
Branch and jump instructions assign to the PC new addresses to change the control flow.
Branch instructions use PC-relative addresses (increment or decrement current value by an offset).

## Slide 6: Branch Instructions
Branch Instructions
Branch = beq rs1, rs2, label
Branch ≠ bne rs1, rs2, label
Branch < blt rs1, rs2, label
Branch ≥ bge rs1, rs2, label
Branch < Unsigned bltu rs1, rs2, label
Branch ≥ Unsigned bgeu rs1, rs2, label

## Slide 7: Branch Pseudoinstructions
Branch Pseudoinstructions
Branch unconditionally b label
Branch = 0 beqz t1, label
Branch ≥ 0 bgez t1, label
Branch > bgt t1, t2, label
Branch > Unsigned bgtu t1, t2, label
Branch > 0 bgtz t1, label
Branch ≤ ble t1, t2, label
Branch ≤ Unsigned bleu t1, t2, label
Branch ≤ 0 blez t1, label
Branch < 0 bltz t1, label
Branch ≠ 0 bnez t1, label

## Slide 8: How Computer Works
Computer
Main Parts:
Control
Datapath
Memory
Input
Output
CPU
Memory
Devices
Input
Output
Control
“Brain”
Datapath
Registers
Bus

## Slide 9: Stored Program Concept
32-bit instructions and data stored in memory
Program is a sequence of instructions
To run a new program:
  Simply load the new program into memory
Program Execution:
  CPU fetches (reads) instructions from memory in sequence
  CPU performs the specified operations

## Slide 10: Stored Program Representation
Assembly Code
lw t0, 32 (t1)
add s1, s0, s2
addi t0, s3, -12
sub t0, t3, t5
Machine Code
0x02032283
0x012404B3
0xFF498293
0x41EE02B3
Memory
Stored Program
Address
…
0x00400000
0x00400004
0x00400008
0x0040000С
…
Instructions
…
0x02032283
0x012404B3
0xFF498293
0x41EE02B3
…
Program Counter (PC): keeps track of current instruction

## Slide 11: RISC-V Instructions
Name | Description | Version | Status
Base |  |  | 
RVWMO | Weak Memory Ordering | 2.0 | Ratified
RV32I | Base Integer Instruction Set, 32-bit | 2.1 | Ratified
RV64I | Base Integer Instruction Set, 64-bit | 2.1 | Ratified
RV128I | Base Integer Instruction Set, 128-bit | 1.7 | Open
Extensions |  |  | 
M | Standard Extension for Integer Multiplication and Division | 2.0 | Ratified
A | Standard Extension for Atomic Instructions | 2.1 | Ratified
F | Standard Extension for Single-Precision Floating-Point | 2.2 | Ratified
D | Standard Extension for Double-Precision Floating-Point | 2.2 | Ratified
G | Shorthand for the base integer set (I) and above extensions (MAFD) | N/A | N/A
Q | Standard Extension for Quad-Precision Floating-Point | 2.2 | Ratified
C | Standard Extension for Compressed Instructions | 2.0 | Ratified
ZiCSR | Control and Status Register (CSR) | 2.0 | Ratified
Zifencei | Instruction-Fetch Fence | 2.0 | Ratified
And more standard and custom extensions… |  |  | 

## Slide 12: Design Principles
Design Principle 1: Simplicity favors regularity
  Regularity makes implementation simpler
  Simplicity enables higher performance at lower cost
Design Principle 2: Make the common case fast
  Most common cases affect the performance the most
Design Principle 3: Smaller is faster
  32 registers, fewer instructions
Design Principle 4: Good design demands good compromises
  Different formats complicate decoding, but allow 32-bit instructions uniformly
  Keep formats as similar as possible

## Slide 13: Six Instruction Formats
R-format: instructions using 3 register inputs
  add, xor, mul - arithmetic/logical ops
I-format: instructions with immediates, loads
  addi, lw, jalr, slli
S-format: store instructions
  sw, sb
SB-format: branch instructions
  beq, bge
U-format: instructions with upper immediates
  lui, auipc - upper immediate is 20-bits
UJ-format: the jump instruction
  jal

## Slide 14: R-format Instructions
Arithmetic Instructions
  opcode: operation code
  rd: destination register number
  funct3: 3-bit function code (additional opcode)
  rs1 and rs2: first and second source register 5-bit numbers
  funct7: 7-bit function code (additional opcode)
funct7
rs2
rs1
rd
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
add x9, x20, x21
0000 0001 0101 1010 0000 0100 1011 0011two = 015A04B316
0
21
20
9
0
51
0000000
10101
10100
01001
000
0110011

## Slide 15: I-format Instructions
Immediate arithmetic and load instructions
  rs1: source or base address register number
  immediate: constant operand, or offset added to base address
    2s-complement, sign extended
immediate
rs1
rd
funct3
opcode
12 bits
7 bits
5 bits
5 bits
3 bits
0x123
6
5
0
19
000100100011
00110
00101
000
0010011
addi t0, t1, 123
0001 0010 0011 0011 0000 0010 1001 0011two = 0x1233029316

## Slide 16: S-format Instructions
Different immediate format for store instructions
  rs1: base address register number
  rs2: source operand register number
  immediate: offset added to base address
    Split so that rs1 and rs2 fields always in the same place
imm[11:5]
rs2
rs1
imm[4:0]
funct3
opcode
7 bits
7 bits
5 bits
5 bits
5 bits
3 bits
0
5
6
4
2
35
0000000
00101
00110
00100
010
100011
sw t0, 4(t1)
0000 0000 0101 0011 0010 0010 0010 0011two = 0x0053222316

## Slide 17: SB-format Instructions
Branch instructions specify
  Opcode, two registers, target address
Most branch targets are near branch
  Branch range is +/- 4KB
PC-relative addressing
  Target address = PC + immediate × 2
imm[10:5]
rs2
rs1
imm[4:1]
funct3
opcode
imm[12]
imm[11]
0
1
0
0
99
0
0
2
000000
00001
00000
000
1100011
0
0
0010
beq x0, x1, 0x4
0000 0000 0001 0000 0000 0010 0110 0011 two = 00100263 16
5 bits
5 bits
3 bits
7 bits
5 bits
6 bits
1 bit
1 bit

## Slide 18: U-format Instructions
Upper-immediate values: 20-bit values shifted left by 12 bits
  opcode: operation code
  rd: destination register number
  imm: 20-bit immediate value
imm[31:12]
rd
opcode
20 bits
5 bits
lui x5, 0x12345
0001 0010 0011 0100 0101 0010 1011 0111two = 123452b716
0x12345
5
55
0001 0010 0011 0100 0101
00101
0110111

## Slide 19: UJ-format Instructions
rd
opcode
imm[11]
imm[20]
imm[19:12]
imm[10:1]
7 bits
5 bits
10 bits
8 bits
1 bit
1 bit
5
111
0
0
0
2
00101
1101111
0
0
00000000
0000000010
Jump instructions
  opcode: operation code
  rd: destination link register
  imm: signed offset in multiples of 2 bytes added to PC
  Target address = PC + immediate × 2
  Jump range is +/- 1MB
0000 0000 0100 0000 0000 0010 1110 1111two = 004002ef16
jal x5, 0x4

## Slide 20: RISC-V Addressing Summary

## Slide 21: Macros

## Slide 22: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero