## Slide 1: Computer Architecture and Operating Systems Lecture 14: Thread-Level Parallelism
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Why We Need Thread-Level Parallelism
Goals
Task-level (process-level) parallelism
  High throughput for independent jobs
Parallel processing program
  Single program run on multiple processors
  Implementations
Hardware multithreading
Multicore microprocessors
  Chips with multiple processors (cores)
Multiprocessors
  Connecting multiple computers to get higher performance
  Scalability, availability, power efficiency

## Slide 3: Challenge: Parallel Programming
Parallel hardware requires parallel software
Parallel software is the problem
Need to get significant performance improvement
  Otherwise, just use a faster uniprocessor, since it is easier
Difficulties
  Partitioning
  Coordination
  Communications overhead

## Slide 4: Threading: Definitions
Process: program running on a computer
  Multiple processes can run at once: e.g., surfing Web, playing music, writing a paper
  Separate virtual memory, stack, registers
Thread: part of a program
  Each process has multiple threads: e.g., a word processor may have threads for typing, spell checking, printing
  Shared virtual memory, separate stack and registers

## Slide 5: Threads in Conventional Uniprocessor (SISD)
One thread runs at once
When one thread stalls (for example, waiting for memory):
  Architectural state of that thread stored
  Architectural state of waiting thread loaded into processor and it runs
  Called context switching (can take thousands of cycles)
Appears to user like all threads running simultaneously
Does not improve performance

## Slide 6: Parallel Processing Challenge: Amdahl’s Law
Sequential part can limit speedup
Example: 100 processors, 90 × speedup?
  Tnew = Tparallelizable/100 + Tsequential
  Speedup =
  Solving: Fparallelizable = 0.999
Need sequential part to be 0.1% of original time

## Slide 7: Scaling Example 1
Workload: sum of 10 scalars, and 10 × 10 matrix sum
  Speed up from 10 to 100 processors
Single processor: Time = (10 + 100) × tadd
10 processors
  Time = 10 × tadd + 100/10 × tadd = 20 × tadd
  Speedup = 110/20 = 5.5 (55% of potential)
100 processors
  Time = 10 × tadd + 100/100 × tadd = 11 × tadd
  Speedup = 110/11 = 10 (10% of potential)
Assumes load can be balanced across processors

## Slide 8: Scaling Example 2
What if matrix size is 100 × 100?
Single processor: Time = (10 + 10000) × tadd
10 processors
  Time = 10 × tadd + 10000/10 × tadd = 1010 × tadd
  Speedup = 10010/1010 = 9.9 (99% of potential)
100 processors
  Time = 10 × tadd + 10000/100 × tadd = 110 × tadd
  Speedup = 10010/110 = 91 (91% of potential)
Assuming load balanced

## Slide 9: Strong vs Weak Scaling
Strong scaling: problem size fixed
  As in the examples
Weak scaling: problem size proportional to number of processors
  10 processors, 10 × 10 matrix
    Time = 20 × tadd
  100 processors, 32 × 32 matrix
    Time = 10 × tadd + 1000/100 × tadd = 20 × tadd
  Constant performance in this example

## Slide 10: Hardware Multithreading
Multiple copies of architectural state
Multiple threads active at once:
  When one thread stalls, another runs immediately
  If one thread can’t keep all execution units busy, another thread can use them
Does not increase instruction-level parallelism (ILP) of single thread, but increases throughput
Intel calls this “hyperthreading”

## Slide 11: Hardware Multithreading
Performing multiple threads of execution in parallel
  Replicate registers, PC, etc.
  Fast switching between threads
Fine-grained multithreading
  Switch threads after each cycle
  Interleave instruction execution
  If one thread stalls, others are executed
Coarse-grained multithreading
  Only switch on long stall (e.g., L2-cache miss)
  Simplifies hardware, but doesn’t hide short stalls (eg, data hazards)
Simultaneous multithreading

## Slide 12: Simultaneous Multithreading
In multiple-issue dynamically scheduled processor
  Schedule instructions from multiple threads
  Instructions from independent threads execute when function units are available
  Within threads, dependencies handled by scheduling and register renaming
Example: Intel Pentium-4 HT
  Two threads: duplicated registers, shared function units and caches

## Slide 13: Multithreading Example

## Slide 14: Multiprocessors (MIMD)
Multiple processors (cores) with a method of communication between them
Types:
  Homogeneous: multiple cores with shared memory
  Heterogeneous: separate cores for different tasks (for example, DSP and CPU in cell phone)
  Clusters: each core has own memory system

## Slide 15: Multicores: Shared Memory
SMP: shared memory multiprocessor
  Hardware provides single physical address space for all processors
  Synchronize shared variables using locks
  Memory access time
    UMA (uniform) vs. NUMA (nonuniform)

## Slide 16: Multicores and Cache Coherence
Suppose two CPU cores share a physical address space
  Write-through caches
Time step | Event | CPU A’s cache | CPU B’s cache | Memory
0 |  |  |  | 0
1 | CPU A reads X | 0 |  | 0
2 | CPU B reads X | 0 | 0 | 0
3 | CPU A writes 1 to X | 1 | 0 | 1

## Slide 17: Coherence Defined
Informally: Reads return most recently written value
Formally:
  P writes X; P reads X (no intervening writes)  read returns written value
  P1 writes X; P2 reads X (sufficiently later)  read returns written value
    CPU B reading X after step 3 in example
  P1 writes X, P2 writes X  all processors see writes in the same order
    End up with the same final value for X

## Slide 18: Cache Coherence Protocols
Operations performed by caches in multiprocessors to ensure coherence
  Migration of data to local caches
    Reduces bandwidth for shared memory
  Replication of read-shared data
    Reduces contention for access
Snooping protocols
  Each cache monitors bus reads/writes
Directory-based protocols
  Caches and memory record sharing status of blocks in a directory

## Slide 19: Synchronization: Basic Building Blocks
Atomic exchange
  Swaps register with memory location
Test-and-set
  Sets under condition
Fetch-and-increment
  Reads original value from memory and increments it in memory
Requires read and write in uninterruptable instruction
RISC-V: load reserved/store conditional
  If the memory location specified by the load is changed before the store conditional to the same address, the store conditional fails

## Slide 20: Multiprocessors: Message Passing
Each processor has private physical address space
Hardware sends/receives messages between processors

## Slide 21: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero