## Slide 1: Computer Architecture and Operating Systems Lecture 2: The C Programming Language
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: The C Programming Language
1972-1973: Developed at Bell Labs by Dennis Ritchie to create utilities for Unix
1973: Unix was re-implemented in C
1978: Brian Kernighan and Dennis Ritchie published The C Programming Language
1989/1990: ANSI C and ISO C; 1999: C99; 2011: C11; 2017: C17

## Slide 3: The Application of C Language
C is not a “very high level” language, nor a “big” one, and is not specialized to any particular area of application. But its absence of restrictions and its generality make it more convenient and effective for many tasks than supposedly more powerful languages.
Kernighan and Ritchie
With C we can write programs that allow us to exploit underlying features of the architecture

## Slide 4: C Concepts
Compiler | Creates usable programs from C source code
Typed variables | Must declare the kind of data the variable will contain
Typed functions | Must declare the kind of data returned from the function
Header files (.h) | Allows declaring functions and variables in separate files
Structs | Groups of related values
Enums | Lists of predefined values
Pointers | Aliases to other variables

## Slide 5: C Memory Layout
Program’s address space contains 4 regions:
  Stack: local variables, grows downward
  Heap: space requested via malloc() and used with pointers; resizes dynamically, grows upward
  Static Data: global and static variables, does not grow or shrink
  Code: loaded when program starts, does not change
Stack
Heap
Static Data
Code
Reserved
0x 0000 0000
0x FFFF FFFF
OS prevents accesses between stack and heap (via virtual memory)

## Slide 6: Where Do the Variables Go?
Declared outside a function:
  Static Data
Declared inside a function:
  Stack
    main() is a function
    freed when the function returns
Dynamically allocated:
  Heap
    i.e. malloc (will be covered shortly)
#include <stdio.h>
int varGlobal;
int main() {
int varLocal;
int *varDyn =
malloc(sizeof(int));
}

## Slide 7: Stack
Each stack frame is a contiguous block of memory holding the local variables of a single function
A stack frame includes:
  Location of caller function
  Function arguments
  Space for local variables
Stack pointer (SP) tells where lowest (current) stack frame is
When function ends, stack pointer is moved back (but data remains (garbage!)); frees memory for future stack frames

## Slide 8: Stack
Last In, First Out (LIFO) data structure
int main() {
a(0);
return 1;
}
void a(int m) {
b(1);
}
void b(int n) {
c(2);
d(4);
}
void c(int o) {
printf(“c”);
}
void d(int p) {
printf(“d”);
}
main
a
b
d
Stack Pointer
Stack Pointer
Stack Pointer
Stack Pointer

## Slide 9: Stack Misuse
int *getPtr() {
int y;
y = 3;
return &y;
}
int main () {
int *stackAddr, content;
stackAddr = getPtr();
content = *stackAddr;
printf("%d", content); /* 3 */
content = *stackAddr;
printf("%d", content); /* ? */
}
Never return pointers to local variable from functions!
Your compiler will warn you about this.
Do not ignore such warnings!
printf overwrites stack frames.

## Slide 10: Any Questions?
.text
__start: addi t1, zero, 0x18
addi t2, zero, 0x21
cycle: beq t1, t2, done
slt t0, t1, t2
bne t0, zero, if_less
nop
sub t1, t1, t2
j cycle
nop
if_less: sub t2, t2, t1
j cycle
done: add t3, t1, zero