## Slide 1: Computer Architecture and Operating Systems Lecture 12: Basics of Networking
Andrei Tatarnikov
atatarnikov@hse.ru
@andrewt0301

## Slide 2: Client-Server Architecture
Most network applications are based on the client-server model:
  A server process and one or more client processes
  Server manages some resource
  Server provides service by manipulating resource for clients
  Server activated by request from client (vending machine analogy)
Client
process
Server
process
1. Client sends request
3. Server sends response
4. Client
handles
response
2. Server
handles
request
Resource
Note: clients and servers are processes running on hosts
(can be the same or different hosts)

## Slide 3: Hardware Organization of a Network Host
main
memory
I/O
bridge
MI
ALU
register file
CPU chip
system bus
memory bus
disk
controller
graphics
adapter
USB
controller
mouse
keyboard
monitor
disk
I/O bus
Expansion slots
network
adapter
network

## Slide 4: Computer Networks
A network is a hierarchical system of boxes and wires organized by geographical proximity
  SAN (System Area Network) spans cluster or machine room
    Switched Ethernet, Quadrics QSW, …
  LAN (Local Area Network) spans a building or campus
    Ethernet is most prominent example
  WAN (Wide Area Network) spans country or world
    Typically high-speed point-to-point phone lines
An internetwork (internet) is an interconnected set of networks
  The Global IP Internet (uppercase “I”) is the most famous example of an internet (lowercase “i”)
Let us see how an internet is built from the ground up

## Slide 5: Lowest Level: Ethernet Segment
Ethernet segment consists of a collection of hosts connected by wires (twisted pairs) to a hub
Spans room or floor in a building
Operation
  Each Ethernet adapter has a unique 48-bit address (MAC address)
    E.g., 00:16:ea:e3:54:e6
  Hosts send bits to any other host in chunks called frames
  Hub slavishly copies each bit from each port to every other port
    Every host sees every bit
    Note: Hubs are on their way out. Bridges (switches, routers) became cheap enough to replace them
host
host
host
hub
100 Mb/s
100 Mb/s
port

## Slide 6: Next Level: Bridged Ethernet Segment
Spans building or campus
Bridges cleverly learn which hosts are reachable from which ports and then selectively copy frames from port to port
host
host
host
host
host
hub
hub
bridge
100 Mb/s
100 Mb/s
host
host
hub
100 Mb/s
100 Mb/s
1 Gb/s
host
host
host
bridge
host
host
hub
A
B
C
X
Y

## Slide 7: Conceptual View of LANs
For simplicity, hubs, bridges, and wires are often shown as a collection of hosts attached to a single wire:
host
host
host
...

## Slide 8: Next Level: Internets
Multiple incompatible LANs can be physically connected by specialized computers called routers
The connected networks are called an internet (lower case)
host
host
host
...
host
host
host
...
WAN
WAN
LAN 1 and LAN 2 might be completely different, totally incompatible
(e.g., Ethernet, Fibre Channel, 802.11*, T1-links, DSL, …)
router
router
router
LAN 1
LAN 2

## Slide 9: Logical Structure of Internet
Ad hoc interconnection of networks
  No particular topology
  Vastly different router & link capacities
Send packets from source to destination by hopping through networks
  Router forms bridge from one network to another
  Different packets may take different routes
router
router
router
router
router
router
host
host

## Slide 10: The Notion of an Internet Protocol
How is it possible to send bits across incompatible LANs and WANs?
Solution: protocol software running on each host and router
  Protocol is a set of rules that governs how hosts and routers should cooperate when they transfer data from network to network.
  Smooths out the differences between the different networks

## Slide 11: What Does an internet Protocol Do?
Provides a naming scheme
  An internet protocol defines a uniform format for host addresses
  Each host (and router) is assigned at least one of these internet addresses that uniquely identifies it
Provides a delivery mechanism
  An internet protocol defines a standard transfer unit (packet)
  Packet consists of header and payload
    Header: contains info such as packet size, source and destination addresses
    Payload: contains data bits sent from source host

## Slide 12: Transferring Internet Data Via Encapsulation
LAN2
protocol
software
client
LAN1
adapter
Host A
LAN1
data
(1)
data
PH
FH1
(4)
data
PH
FH2
(6)
data
(8)
data
PH
FH2
(5)
LAN2 frame
protocol
software
LAN1
adapter
LAN2
adapter
Router
data
PH
(3)
FH1
data
PH
FH1
(2)
internet packet
LAN1 frame
(7)
data
PH
FH2
protocol
software
server
LAN2
adapter
Host B
PH: Internet packet header
FH: LAN frame header

## Slide 13: Other Issues
We are glossing over a number of important questions:
  What if different networks have different maximum frame sizes? (segmentation)
  How do routers know where to forward frames?
  How are routers informed when the network topology changes?
  What if packets get lost?
These (and other) questions are addressed by the area of systems known as computer networking

## Slide 14: Global IP Internet (upper case)
Most famous example of an internet
Based on the TCP/IP protocol family
  IP (Internet Protocol) :
    Provides basic naming scheme and unreliable delivery capability of packets (datagrams) from host-to-host
  UDP (Unreliable Datagram Protocol)
    Uses IP to provide unreliable datagram delivery from process-to-process
  TCP (Transmission Control Protocol)
    Uses IP to provide reliable byte streams from process-to-process over connections
Accessed via a mix of Unix file I/O and functions from the sockets interface

## Slide 15: Organization of an Internet Application
TCP/IP
Client
Network
adapter
Global IP Internet
TCP/IP
Server
Network
adapter
Internet client host
Internet server host
Sockets interface
(system calls)
Hardware interface
(interrupts)
User code
Kernel code
Hardware
and firmware

## Slide 16: A Programmer’s View of the Internet
1. Hosts are mapped to a set of 32-bit IP addresses
  128.2.203.179
2. The set of IP addresses is mapped to a set of identifiers called Internet domain names
  128.2.203.179 is mapped to www.cs.cmu.edu
3. A process on one Internet host can communicate with a process on another Internet host over a connection

## Slide 17: Aside: IPv4 and IPv6
The original Internet Protocol, with its 32-bit addresses, is known as Internet Protocol Version 4 (IPv4)
1996: Internet Engineering Task Force (IETF) introduced Internet Protocol Version 6 (IPv6) with 128-bit addresses
  Intended as the successor to IPv4
As of 2015, vast majority of Internet traffic still carried by IPv4
  Only 4% of users access Google services using IPv6.
We will focus on IPv4, but will show you how to write networking code that is protocol-independent.

## Slide 18: IP Addresses
32-bit IP addresses are stored in an IP address struct
  IP addresses are always stored in memory in network byte order (big-endian byte order)
  True in general for any integer transferred in a packet header from one machine to another.
    E.g., the port number used to identify an Internet connection.
/* Internet address structure */
struct in_addr {
uint32_t s_addr; /* network byte order (big-endian) */
};

## Slide 19: Dotted Decimal Notation
By convention, each byte in a 32-bit IP address is represented by its decimal value and separated by a period
    IP address: 0x8002C2F2 = 128.2.194.242
Use getaddrinfo and getnameinfo functions (described later) to convert between IP addresses and dotted decimal format.

## Slide 20: Internet Domain Names
.net
.edu
.gov
.com
cmu
berkeley
mit
cs
ece
whaleshark
128.2.210.175
ics
unnamed root
pdl
www
128.2.131.66
amazon
www
176.32.98.166
First-level domain names
Second-level domain names
Third-level domain names

## Slide 21: Domain Naming System (DNS)
The Internet maintains a mapping between IP addresses and domain names in a huge worldwide distributed database called DNS
Conceptually, programmers can view the DNS database as a collection of millions of host entries.
  Each host entry defines the mapping between a set of domain names and IP addresses.
  In a mathematical sense, a host entry is an equivalence class of domain names and IP addresses.

## Slide 22: Properties of DNS Mappings
Can explore properties of DNS mappings using nslookup
  Output edited for brevity
Each host has a locally defined domain name localhost which always maps to the loopback address 127.0.0.1
Use hostname to determine real domain name of local host:
linux> nslookup localhost
Address: 127.0.0.1
linux> hostname
whaleshark.ics.cs.cmu.edu

## Slide 23: Properties of DNS Mappings (cont)
Simple case: one-to-one mapping between domain name and IP address:
Multiple domain names mapped to the same IP address:
linux> nslookup whaleshark.ics.cs.cmu.edu
Address: 128.2.210.175
linux> nslookup cs.mit.edu
Address: 18.62.1.6
linux> nslookup eecs.mit.edu
Address: 18.62.1.6

## Slide 24: Properties of DNS Mappings (cont)
Multiple domain names mapped to multiple IP addresses:
Some valid domain names don’t map to any IP address:
linux> nslookup www.twitter.com
Address: 199.16.156.6
Address: 199.16.156.70
Address: 199.16.156.102
Address: 199.16.156.230
linux> nslookup twitter.com
Address: 199.16.156.102
Address: 199.16.156.230
Address: 199.16.156.6
Address: 199.16.156.70
linux> nslookup ics.cs.cmu.edu
*** Can't find ics.cs.cmu.edu: No answer

## Slide 25: Internet Connections
Clients and servers communicate by sending streams of bytes over connections. Each connection is:
  Point-to-point: connects a pair of processes.
  Full-duplex: data can flow in both directions at the same time,
  Reliable: stream of bytes sent by the source is eventually received by the destination in the same order it was sent.
A socket is an endpoint of a connection
  Socket address is an IPaddress:port pair
A port is a 16-bit integer that identifies a process:
  Ephemeral port: Assigned automatically by client kernel when client makes a connection request.
  Well-known port: Associated with some service provided by a server (e.g., port 80 is associated with Web servers)

## Slide 26: Well-known Ports and Service Names
Popular services have permanently assigned well-known ports and corresponding well-known service names:
  echo server: 7/echo
  ssh servers: 22/ssh
  email server: 25/smtp
  Web servers: 80/http
Mappings between well-known ports and service names is contained in the file /etc/services on each Linux machine.

## Slide 27: Anatomy of a Connection
A connection is uniquely identified by the socket addresses of its endpoints (socket pair)
  (cliaddr:cliport, servaddr:servport)
Connection socket pair
(128.2.194.242:51213, 208.216.181.15:80)
Server
(port 80)
Client
Client socket address
128.2.194.242:51213
Server socket address
208.216.181.15:80
Client host address
128.2.194.242
Server host address
208.216.181.15
51213 is an ephemeral port
allocated by the kernel
80 is a well-known port
associated with Web servers

## Slide 28: Using Ports to Identify Services
Web server
(port 80)
Client host
Server host 128.2.194.242
Echo server
(port 7)
Service request for
128.2.194.242:80
(i.e., the Web server)
Web server
(port 80)
Echo server
(port 7)
Service request for
128.2.194.242:7
(i.e., the echo server)
Kernel
Kernel
Client
Client

## Slide 29: Basic Internet Components
Internet backbone:
  collection of routers (nationwide or worldwide) connected by high-speed point-to-point networks
Internet Exchange Points (IXP):
  router that connects multiple backbones (often referred to as peers)
  Also called Network Access Points (NAP)
Regional networks:
  smaller backbones that cover smaller geographical areas (e.g., cities or states)
Point of presence (POP):
  machine that is connected to the Internet
Internet Service Providers (ISPs):
  provide dial-up or direct access to POPs

## Slide 30: Internet Connection Hierarchy
IXP
IXP
Backbone
Backbone
Backbone
Backbone
IXP
POP
POP
POP
Regional net
POP
POP
POP
POP
POP
Small Business
Big Business
ISP
POP
POP
POP
POP
Pgh employee
Cable
modem
DC employee
POP
T3
T1
ISP (for individuals)
POP
DSL
T1
Colocation
sites
Private
“peering”
agreements
between
two backbone
companies
often bypass
IXP

## Slide 31: IP Address Structure
IP (V4) Address space divided into classes:
Network ID Written in form w.x.y.z/n
  n = number of bits in host address
  E.g., CMU written as 128.2.0.0/16
    Class B address
Unrouted (private) IP addresses:
  10.0.0.0/8 172.16.0.0/12 192.168.0.0/16
Class A
Class B
Class C
Class D
Class E
0 1 2 3 8 16 24 31
0
Net ID
Host ID
Host ID
Host ID
Net ID
Net ID
Multicast address
Reserved for experiments
1
0
1
0
1
1
1
0
1
1
1
1
1